## Slide 1
Robust robot navigation against imperfect sensor data
20203397 Hyeongyeol Ryu
20203408 Minsung Yoon
20203474 Sebin Lee
2020.11.12
Notes: 1

## Slide 2: Table of contents
Introduction & Research goal
Related Work
Background
Our approach
Current progress & Future work
Schedule & Role

## Slide 3: Table of contents
Introduction & Research goal
Related Work
Background
Our approach
Current progress & Future work
Schedule & Role

## Slide 4: Introduction
These days, many mobile-robots are around humans
Mobile service robots

## Slide 5: Introduction
These days, many mobile-robots are around humans
  One of the most essential abilities of the robots is the autonomous navigation
  Using its on-board sensors (e.g., LIDAR, RGB-D camera)
Reach the goal while avoiding collision
Autonomous navigation

## Slide 6: Introduction
But the problem is …
  What if the robot could not get perfect sensor data because of
    Humans’ mistakes (e.g., ice-cream, gum, curiosity, prank)
    Papers/Leaves blowing in the wind
    Sudden malfunction
This may cause temporal occlusion, limited FOV problems
Collision!

## Slide 7: Research goal
Our goal is to propose robust navigation method dealing with unexpected accidents by occlusion/limited FOV
Q: How can we solve this?
Goal
Goal

## Slide 8: Table of contents
Introduction & Research goal
Related Work
Background
Our approach
Current progress & Future work
Schedule & Role

## Slide 9: Related Work
There have not been related works that target this problem
Instead, we introduce some papers trying to solve similar problems
  Navigation with limited FOV [ICRA19]
  Navigation under uncertainty [ICRA20]

## Slide 10: Related Work
[1]Deep Reinforcement Learning of Navigation in a Complex and Crowded Environment with a Limited Field of View [ICRA19]
FOV: 270⁰
FOV: 120⁰
FOV: 90⁰
LSTM + Local Map [90⁰]
Only CNN [90, 120, 180⁰]

## Slide 11: Related Work
[2]Learning Resilient Behaviors for Navigation Under Uncertainty [ICRA20]
  Navigation under two uncertainty:
  Lidar sensor data uncertainty + Robot system uncertainty
High uncertainty
Low uncertainty
 | Efficiency | Safety
Over-confident | High | Low
Over-conservative | Low | High
Balanced policy | High | High

## Slide 12: Table of contents
Introduction & Research goal
Related Work
Background
Our approach
Current progress & Future work
Schedule & Role

## Slide 13: Background
Global Path Planning  Navigation (Local planning or control)
Black Line: Global path Red Line: Navigation (Local planning or control)
For robustness of navigation
Consider :
1. Temporal occlusion 2. Partially damaged FOV

## Slide 14: Table of contents
Introduction & Research goal
Related Work
Background
Our approach
Current progress & Future work
Schedule & Role

## Slide 15: Our approach
Problems
Problem1: Temporal occlusion
Problem2: Partially damaged FOV
Problem Modeling and RL
&
Novel Architecture
Normal

## Slide 16: Our approach: Problem Modeling and RL
Problem Modeling
2D Lidar observation
Usual case
Problem case

## Slide 17: Our approach: Problem Modeling and RL
Problem Modeling
Modeling
2D Lidar observation
Occlusion modeling parameters:

## Slide 18: Our approach: Problem Modeling and RL
RL Problem Definition
  Robot : Differential drive robot.
  Setting : Dynamic environment and Sensor could be partially damaged any time.
  Observation : 2D Lidar sensor data + robot’s current state ()
  Action : linear & angular velocity
  Reward : Reach to the goal + avoid collision

## Slide 19: Our approach: Novel Architecture
Stacked
LIDAR observation
Robot’s state
Conv1
Goal location
from current state
…
Partition
Conv1
Conv2
Conv3
ConvK
…
Attention
Module
Conv2
FC
FC
FC
LSTM
Output
FC
Linear &
Angular velocity
Observation embeddings

## Slide 20: Our approach: Novel Architecture
Stacking N frames of sequential sensor input
Partitioning stacked sensor data into K splits
Stacked N frames of sensor data
(Robust to temporal occlusion)
N

## Slide 21: Our approach: Novel Architecture
Stacking N frames of sequential sensor input
Partitioning stacked sensor data into K splits
Stacked N frames of sensor data
(Robust to temporal occlusion)
N
…
K
…

## Slide 22: Our approach: Novel Architecture
Apply the individual CNNs into the K splits of partitioned sensor data.
…
K
Conv1
Conv2
Conv3
ConvK
Partitioned sensor data
Feature maps

## Slide 23: Our approach: Novel Architecture
Extract attention weight at each partition
…
K
Conv1
Conv2
Conv3
ConvK
Partitioned sensor data
Feature maps
Attention
Module
…
Feature Attention

## Slide 24: Our approach: Novel Architecture
Weighted sum of feature maps
…
K
Conv1
Conv2
Conv3
ConvK
Partitioned sensor data
Feature maps
Attention
Module
…
Feature Attention

## Slide 25: Our approach: Novel Architecture
Stacked
LIDAR observation
Robot’s state
Conv1
Goal location
from current state
…
Partition
Conv1
Conv2
Conv3
ConvK
…
Attention
Module
Conv2
FC
FC
FC
LSTM
Output
FC
Linear &
Angular velocity
Observation embeddings

## Slide 26: Our approach
Expected results
 | Navigation (without Ours) | Navigation (with Ours)
Collision rate | High | Low
Success(arrival) rate | Low | High
Without Ours
With Ours

## Slide 27: Table of contents
Introduction & Research goal
Related Work
Background
Our approach
Current progress & Future work
Schedule & Role

## Slide 28: Current progress
Modeling robot with sensor

## Slide 29: Current progress
Test RL agent in simple environment

## Slide 30: Current progress
Training RL agent in dynamic environment

## Slide 31: Future work
Problem modeling
Build novel architecture

## Slide 32: Table of contents
Introduction & Research goal
Related Work
Background
Our approach
Current progress & Future work
Schedule & Role

## Slide 33: Schedule & Role
 | ~10.27 | ~11.12 | ~11.19 | ~11.26 | ~12.03 | ~12.08
Survey problem |  |  |  |  |  | 
Build training environment |  |  |  |  |  | 
Mid-term presentation |  |  |  |  |  | 
Build architecture |  |  |  |  |  | 
Training RL agent |  |  |  |  |  | 
Testing & collecting results |  |  |  |  |  | 
Final presentation |  |  |  |  |  | 
today

## Slide 34: Schedule & Role
 | Survey problem | Build training environment | Mid-term presentation | Build architecture | Defining reward function | Training RL agent | Testing & collecting results | Final presentation
Hyeongyeol | O | O | O |  |  | O | O | O
Minsung | O |  | O |  | O | O | O | O
Sebin | O |  | O | O |  | O | O | O

## Slide 35: Reference
Papers
[1] J. Choi, K. Park, M. Kim and S. Seok, "Deep Reinforcement Learning of Navigation in a Complex and Crowded Environment with a Limited Field of View," 2019 International Conference on Robotics and Automation (ICRA), Montreal, QC, Canada, 2019, pp. 5993-6000, doi: 10.1109/ICRA.2019.8793979.
[2] T. Fan, P. Long, W. Liu, J. Pan, R. Yang and D. Manocha, "Learning Resilient Behaviors for Navigation Under Uncertainty," 2020 IEEE International Conference on Robotics and Automation (ICRA), Paris, France, 2020, pp. 5299-5305, doi: 10.1109/ICRA40945.2020.9196785.
[3] A. Faust et al., "PRM-RL: Long-range Robotic Navigation Tasks by Combining Reinforcement Learning and Sampling-Based Planning," 2018 IEEE International Conference on Robotics and Automation (ICRA), Brisbane, QLD, 2018, pp. 5113-5120, doi: 10.1109/ICRA.2018.8461096.
[4] J. Jin, N. M. Nguyen, N. Sakib, D. Graves, H. Yao and M. Jagersand, "Mapless Navigation among Dynamics with Social-safety-awareness: a reinforcement learning approach from 2D laser scans," 2020 IEEE International Conference on Robotics and Automation (ICRA), Paris, France, 2020, pp. 6979-6985, doi: 10.1109/ICRA40945.2020.9197148.
[5] F. Leiva and J. Ruiz-del-Solar, "Robust RL-Based Map-Less Local Planning: Using 2D Point Clouds as Observations," in IEEE Robotics and Automation Letters, vol. 5, no. 4, pp. 5787-5794, Oct. 2020, doi: 10.1109/LRA.2020.3010732.
[6] C. Chen, Y. Liu, S. Kreiss and A. Alahi, "Crowd-Robot Interaction: Crowd-Aware Robot Navigation With Attention-Based Deep Reinforcement Learning," 2019 International Conference on Robotics and Automation (ICRA), Montreal, QC, Canada, 2019, pp. 6015-6022, doi: 10.1109/ICRA.2019.8794134.
[7] Jin, Jun, et al. "Mapless Navigation among Dynamics with Social-safety-awareness: a reinforcement learning approach from 2D laser scans." 2020 IEEE International Conference on Robotics and Automation (ICRA). IEEE, 2020.
[8] Gao, Wei, et al. "Intention-net: Integrating planning and deep learning for goal-directed autonomous navigation." arXiv preprint arXiv:1710.05627 (2017).
[9] Everett, Michael, Yu Fan Chen, and Jonathan P. How. "Motion planning among dynamic, decision-making agents with deep reinforcement learning." 2018 IEEE/RSJ International Conference on Intelligent Robots and Systems (IROS). IEEE, 2018.
Media Contents
[1] Professionelle mobile Service-Roboter - MetraLabs
[2] HoLLiE Mobile Service Robot Can Bend to Reach the Floor – roboticgizmos
[3] https://www.artificialinventive.com/blog/
[4] https://developer.softbankrobotics.com/blog/crowdbot-safe-navigation-robots-dense-crowds

## Slide 36: Thank you for watching
Hope you enjoyed! 🤣
Q & A